## Slide 3
BEAMnrc models a stack of component modules (CM)
CM 1
CM 2
CM 3
CM 4
CM 5
CM 6
CM 7
z

## Slide 4
BEAMnrc models a stack of component modules (CM)
z
CM 1
CM 2
CM 3
CM 4
CM 5
CM 6
CM 7
Zmin for CM 3
default medium

## Slide 5
Each component module has a type and a name
CM 1: SLABS “target”
CM 2: CONS3R “primcoll”
CM 3: FLATFILT “flattenf”
CM 4: CHAMBER “chamber”
CM 5: MIRROR “mirror”
CM 6: JAWS “secjaws”
CM 7: SLABS “airslab”
Rmax for CM 7

## Slide 6
Edit CM parameters with beamnrc_gui
CM 1: SLABS “target”
CM 2: CONS3R “primcoll”
CM 3: FLATFILT “flattenf”
CM 4: CHAMBER “chamber”
CM 5: MIRROR “mirror”
CM 6: JAWS “secjaws”
CM 7: SLABS “airslab”
Rmax for CM 7

## Slide 7
Edit CM parameters with beamnrc_gui
CM 1: SLABS “target”
CM 2: CONS3R “primcoll”
CM 3: FLATFILT “flattenf”
CM 4: CHAMBER “chamber”
CM 5: MIRROR “mirror”
CM 6: JAWS “secjaws”
CM 7: SLABS “airslab”
Rmax for CM 7

## Slide 8
Define the accelerator in a .module text file
Create text file $EGS_HOME/beamnrc/spec_modules/mylinac.module This file specifies what component modules you want inside your accelerator, and their names. For example:
Run beam_build.exe mylinac (no extension) This program collects the source code for your accelerator inside a new application directory $EGS_HOME/BEAM_mylinac/
Launch beamnrc_gui and load your accelerator This program is a Tcl/Tk graphical user interface to visualize an accelerator and edit all the simulation parameters.
CM names: SLABS CONS3R JAWS SLABS
Identifiers: mytarget mycollim myjaws myair

## Slide 9
Edit your BEAMnrc input file with beamnrc_gui

## Slide 10
Edit your BEAMnrc input file with beamnrc_gui

## Slide 11
Edit your BEAMnrc input file with beamnrc_gui

## Slide 12
Edit your BEAMnrc input file with beamnrc_gui

## Slide 13
BEAMnrc scoring concepts
Dose zone: A collection of geometrical regions for which dose is reported as a whole at the end of the simulation. You define which geometrical regions are associated to each doze zone in the CM inputs.
Scoring plane: A plane positioned below any CM to: a) calculate number, fluence, average energy and angle, in user-defined planar scoring zone; and b) save all particles reaching the plane to a phase space file.
Latch bits: The latch variable is a bit field travelling with a particle to keep track where the particle and its ancestors have been, or where they have interacted.

## Slide 14
1. Dose zone
Somewhere in the CM input, for each geometrical region, there is a dose zone input:
CM 1
CM 2
CM 3
CM 4
12
12
12
12
Suppose I set the dose zone to 12 for all 4 jaw regions in this diagram.
Then BEAMnrc will output a dose summary for the dose zone 12, which will give the dose deposited in all 4 regions, as a whole.
(Dose zones don’t have to be assigned.)

## Slide 15
2. Scoring plane: a) analyze fluence
z
CM 1
CM 2
CM 3
CM 4
CM 5
CM 6
CM 7
scoring plane 1 (CM 3)
scoring plane 2 (CM 5)
scoring plane 3 (CM7)
You can define up to 3 scoring planes, located at the bottom of any CM. The properties of particles reaching a scoring plane are “recorded”.

## Slide 16
2. Scoring plane: a) analyze fluence
Each scoring plane can be further divided in radial or square scoring zones.
z
CM 1
CM 2
CM 3
CM 4
CM 5
CM 6
CM 7
1
2
3
BEAMnrc reports number, fluence, average energy and angle for each scoring zone.

## Slide 17
2. Scoring plane: b) save particles to file
Scoring plane

## Slide 18
3. “Latch” but not least: latch bits
1
2
3
4
5
6
7
8
10
11
12
13
14
15
16
17
18
20
21
22
23
9
19
region 53
regions 2, 42, 13, 9
When you design a component module, you can associate any geometrical region with any given latch bit:
If you can operate a light switch, you understand latch! The latch variable is a set of 32 bits that particles carry around with them. We care about bits 1–23.
default

## Slide 19
3. “Latch” but not least: latch bits
1
2
3
4
5
6
7
8
10
11
12
13
14
15
16
17
18
20
21
22
23
9
19
particle passes in region 53
regions 2, 42, 13, 9
region 53
When you design a component module, you can associate any geometrical region with any given latch bit:
If you can operate a light switch, you understand latch! The latch variable is a set of 32 bits that particles carry around with them. We care about bits 1–23.
default

## Slide 20
If you can operate a light switch, you understand latch! The latch variable is a set of 32 bits that particles carry around with them. We care about bits 1–23.
3. “Latch” but not least: latch bits
1
2
3
4
5
6
7
8
10
11
12
13
14
15
16
17
18
20
21
22
23
9
19
region 53
particle passes in region 2 or 42 or 13 or 9
regions 2, 42, 13, 9
When you design a component module, you can associate any geometrical region with any given latch bit:
default
particle passes in region 53

## Slide 21
If you can operate a light switch, you understand latch! The latch variable is a set of 32 bits that particles carry around with them. We care about bits 1–23.
3. “Latch” but not least: latch bits
1
2
3
4
5
6
7
8
10
11
12
13
14
15
16
17
18
20
21
22
23
9
19
If the particle passes through any region associated with a latch bit, this bit is turned on (set to 1). This is a bit filter for dose components and analysis!
region 53
regions 2, 42, 13, 9
When you design a component module, you can associate any geometrical region with any given latch bit:
likely
particle passes in region 2 or 42 or 13 or 9
particle passes in region 53
default

## Slide 22
3. “Latch” but not least: latch inheritance
2
3
1
4
5
6
...
latch bits
latch bit associations (not region numbers!)

## Slide 23
3. “Latch” but not least: latch inheritance
2
3
1
...
4
5
6
latch bit associations (not region numbers!)

## Slide 24
4
5
6
3. “Latch” but not least: latch inheritance
2
3
1
...
latch bit associations (not region numbers!)

## Slide 25
4
5
6
3. “Latch” but not least: latch inheritance
2
3
1
...
...
secondary
non-inherited latch: bits are set by passage, and no latch information is passed on to secondaries.
latch bit associations (not region numbers!)

## Slide 26
4
5
6
3. “Latch” but not least: latch inheritance
2
3
1
...
...
non-inherited latch: bits are set by passage, and no latch information is passed on to secondaries.
inherited latch, by passage:
bits are set by passage, and latch is copied to newly created secondary particles.
secondary
latch bit associations (not region numbers!)

## Slide 27
4
5
6
3. “Latch” but not least: latch inheritance
2
3
1
non-inherited latch: bits are set by passage, no latch information is passed on to secondaries.
inherited latch, by passage:
bits are set by passage, and latch is copied to newly created secondary particles.
inherited latch, by interaction:
for photons, a bit is only set if the photon interacts in the associated region(s).
secondary photon
...
latch bit associations (not region numbers!)

## Slide 28
Edit your BEAMnrc input file with beamnrc_gui

## Slide 29
BEAMnrc main inputs: everything except geometry
Help!

## Slide 30
BEAMnrc main inputs: the “easy” ones

## Slide 31
Default medium

## Slide 32
Number of histories and seeds
NCASE

## Slide 33
Number of histories and seeds
Remember: using the same seeds will run exactly the same simulation (on the same hardware)
NCASE

## Slide 34
Source particle can be electron, photon or positron

## Slide 35
BEAMnrc offers 16 different source types

## Slide 36
Example: source 0, parallel beam from the front
See the BEAMnrc manual for the precise meaning
of the inputs

## Slide 37
Sources will be discussed in the next lecture

## Slide 38
Default ECUT and PCUT

## Slide 39
Default ECUT and PCUT
Global ECUT and PCUT are applied to all regions by default. Input value is in MeV.
They can be overridden (increased) in each region, via CM input parameters.
It is common in linacs to have larger cutoff values because we care about what reaches the bottom of the linac.
For example, ECUT = 0.700 PCUT = 0.189 is a common choice (this is why there is a 700icru pegs data set!)

## Slide 40
EGSnrc parameters discussed in previous lectures

## Slide 41
BEAMnrc main inputs: VRTs discussed in other lecture

## Slide 42
BEAMnrc main inputs: scoring and output

## Slide 43
BEAMnrc main inputs: scoring planes
z
CM 1
CM 2
CM 3
CM 4
CM 5
CM 6
CM 7
1
2

## Slide 44
BEAMnrc main inputs: scoring planes

## Slide 45
BEAMnrc main inputs: scoring planes

## Slide 46
z
CM 1
CM 2
CM 3
CM 4
CM 5
CM 6
CM 7
1
2
By default, phase space is stored at scoring planes
IO_OPT

## Slide 47
z
CM 1
CM 2
CM 3
CM 4
CM 5
CM 6
CM 7
1
2
By default, phase space is stored at scoring planes
IO_OPT
Format | File names
EGSnrc | inputfile.egsphsp1
IAEA | inputfile.1.IAEAheader inputfile.1.IAEAphsp

## Slide 48
Inspect particle histories in detail with IWATCH
Output to screen or .egslog file
IWATCH

## Slide 49
Data arrays must be stored for recovery
IRESTART
IDAT
By default, run a fresh simulation
Recover, or run more histories

## Slide 50
By default, RNG seeds are stored at start of batch
BEAMnrc stores seeds periodically, to recover from crashes or improve statistics.
Storing the seeds at every history is very slow! Stored in .egsrns file

## Slide 51
Data arrays must be stored for recovery
IRESTART
IDAT
By default, run a fresh simulation
Recover, or run more histories
Combine .egsdat files from parallel runs and analyze the results

## Slide 52
Data arrays must be stored for recovery
IRESTART
IDAT
By default, run a fresh simulation
Recover, or run more histories
Combine .egsdat files from parallel runs and analyze the results
Restart and analysis require:
No reason to turn this off (unless you have thousands of doze scoring zones)

## Slide 53
4
5
6
2
3
1
...
...
latch bit associations
secondary
By default, LATCH bits are inherited, and by passage

## Slide 54
You can keep track of the last interaction position
IZLAST

## Slide 55
You can keep track of the last interaction position
IZLAST
in phase space file!

## Slide 56
Beyond total dose: components and contaminants
As soon as a particle of this type enters the specified CM, the dose resulting from it (and descendants) is tallied under contaminant dose.
ICM_CONTAM

## Slide 57
You can keep track of the last interaction position
IZLAST

## Slide 58
LATCH bits are particle filters for dose components
contaminant
bit region number where secondary was created
bit region where particle passed or interacted
when inherited, settings are “cumulative”

## Slide 59
LATCH bits are particle filters for dose components
#1
#2

## Slide 60
bit regions are assigned during CM definition (see CM lecture)
bits 1-23 can be assigned to regions
by default regions are assigned to bit 23
LATCH bits are particle filters for dose components
#1

## Slide 61
Limits can be changed, but you have to recompile
Macro | Description | Default
$MAX_CMs | maximum number of CMs | 24
$MXMED | maximum number of media | 12
$MXREG | maximum number of regions | 3 000
$MXSTACK | maximum number of particles on stack | 10 000
$MAXBRSPLIT | maximum brems splitting number | 2 000
$MAX_DOSE_ZONE | maximum number of dose zones | 1 500
$MAX_SC_PLANES | maximum number of scoring planes | 3
$MAX_SC_ZONES | maximum number of scoring zones | 5
Defined in $OMEGA_HOME/beamnrc/beamnrc_user_macros.mortran
​Copy into $EGS_HOME/BEAM_myaccel directory to change for myaccel only
Need to recompile (make) myaccel to apply changes

## Slide 62
Conclusions
BEAMnrc is installed by default as part of EGSnrc.
BEAMnrc is a well-vetted workhorse EGSnrc application builder for modelling “linear accelerators” (stacked components).
Recommendation: use beamnrc_gui to edit your input files.
BEAMnrc offers quite a complete library of linac component modules.
Compile BEAMnrc as a shared library to use as a source (make library).
BEAMnrc offers some aggressive variance reduction techniques.
You can implement your own component modules or sources, based on existing ones (in MORTRAN).