## Slide 2: beamdp analyzes data stored in (2D) phase space files
Y
X
fluence/inicdent particle

## Slide 3: Spatial vs Spectral quantities

## Slide 4
Spatial fields
circular or square fields centered at origin divided into bins of equal area
X
Y
X
Y

## Slide 5
Spatial fields
rectangular fields anywhere on the phase space plane divided into bins of equal width
bins (plots) oriented in X- or Y-direction
X
X
Y
Ymin
Ymax
Xmin
Xmax

## Slide 6
Spectral fields
Rectangle anywhere on the plane or annular region centered at origin
X
X
Y
Ymin
Ymax
Xmin
Xmax
X
Y
Rmax
Rmin

## Slide 7
Spectral quantities
Specify range and number of bins
e.g. Angular distribution:
For angular distribution only: also specify an energy range

## Slide 8: LATCH Review I
From beamnrc_gui:
LATCH is a 32-bit integer variable that travels with the particle
LATCH bits are associated with regions in BEAMnrc or other application

## Slide 9: LATCH Review II
Set if brems or positron annihiliation occurred
Set if particle interacted/passed through corresponding region
For secondaries: 24-28, downshifted by 24 bits, store the bit (1-23) associated with the region where they were created
For primaries: not set
In BEAMnrc, AIR regions default to bit 23

## Slide 10
BEAMDP LATCH filtering: inclusive/exclusive for bits
Include the particle only if any “inclusive bits” are set
AND none of the “Exclusive bits” are set

## Slide 11
Latch filtering: exclusive for bits
Include the particle only if none of the “exclusive bits” are set

## Slide 12
Latch filtering: inclusive for regions
Include only secondary particles originating in regions associated with “inclusive bits”
LATCH bits associted with regions in BEAMnrc or other application
Stored in bits 24-28 of LATCH
Region 23 is usually reserved for air

## Slide 13
Latch filtering: exclusive for regions
Include only secondary particles not originating in regions associated with “exclusive bits”

## Slide 14: Input/Output files
Input phase space data
Output data file optimized for
plotting with xmgrace/qtgrace
Use the same output file for the option to add data to an existing plot

## Slide 15: Plot type
point plot
histogram

## Slide 16: Fluence type
Z
gi
wi
w = Z-direction cosine
planar fluence =
estimated real fluence
(weight = wti)
=
phase space plane
min. w = 0.08716 (85o)

## Slide 17: Angular distributions
Z
Z=0
phase space plane
angular bin i
solid angle i (rad)

## Slide 18: Example: Derive spectral distribution
Don’t forget to select particle type!

## Slide 19: Example: Derive spectral distribution
statistically-independent histories (i.e. e- incident on target)

## Slide 20: Example: Derive spectral distribution
LATCH bit 1 associated with target
Plot secondary photons

## Slide 21: Example: Derive spectral distribution

## Slide 22: X-Y Scatter plot
defaults to plot all photons

## Slide 24: List parameters for a number of particles

## Slide 25: List parameters for a number of particles